Adjustable Front Suspension

The image with this file is of a front right hand side upper wishbone. This design allows you to alter castor angle with relative ease. However you will need to invest in 2 rose joints, which are not cheap and result in a harder ride than metalistic bushes.

Measurements are for the rose joint on Leg 1 fully screwed in and the rose joint on Leg 2 fully extended (as much as is safe). By simultaneously winding out rose joint 1 and winding in rose joint 2, you will be able to vary the castor angle through a range between 20 and 60.

In order for this design to be possible the mounting brackets on the chassis need to be angled the same as the arms and not perpendicular to the chassis. After adjusting castor you should re-check your camber angle as it will change slightly.

Bottom wishbone is the same as the book.

I also suggest checking the design by chrisdrewnicki for his modified design of the wishbone.

I would like to point out that this design is purely theoretical at present but I fully intend to use this design in my car that I will be starting very soon.

Feel free to email me at aaron_creed@yahoo.com with any ideas, problems etc.

The usual disclaimer applies, best efforts have been made to provide a safe and feasible design but I accept no liability for the design and you use it at our own risk etc.